Shenzhen Concox Information Technology Co. Ltd

GT03A/B

Communication protocol

———————————————————————

Copyright announcement

The copyright of this document is reserved by Huizhou Xinzhongxin Electronic Technical Develop Co., Ltd. Reserve all rights.

Any unauthorized behavior as copying, transmitting part or whole of this document will take all legal obligations.

Content

1. Communication statute	1

1.1 Introduction	1

1.2 Compatibility	1

2. Terms, definitions	1

3. Basic rule	2

4. Data package format	4

4.1 Start Bit	4

4.2 Package Length	4

4.3 Protocol number	4

4.4 Information Contents	5

4.5 Information Serial Number	5

4.6 Error Check	5

4.7 Stop Bit	5

5. Details about Data Packet sent from Terminal to Server	6

5.1 Login Message Packet	6

5.2 GPS information package（0X10）	9

5.3 LBS information package (0x11)	13

5.4 Status info package (0x13)	15

5.5 Combined information packet of GPS, LBS and Status (0X16)	18

5.6 LBS, phone number checking location info package (0X17)	21

5.7	LBS Extension Info Package (0X18)	24

5.8 LBS, Status info package（0X19）	26

5.9 GPS, phone number checking location info package (0X1A)	27

6. Data Packet Sent From Server to Terminal	30

6.1 Command from server to terminal（Setting Command 0X80）	30

6.2 Command sent from server to terminal（checking command 0X81）	32

7. Instruction about login data package and status package	34

8. Appendix A: code fragment of the CRC-ITU lookup table algorithm implemented based on C language	35

9. Appendix B: a fragment of example of data packet of communication protocol	36

10. Appendix C: Complete format of information package	37

# 1. Communication statute

## 1.1 Introduction

This document defines instructions about interface protocol on application layer of vehicles GPS tracker and location-base6d service platform. Related interface protocol only applies in the interaction between the platform and the position terminal.

## 1.2 Compatibility

The applicable platform version is GT03A/B.

# 2. Terms, definitions

| Terms/ab. | English meanings |
| --- | --- |
| CMPP | China Mobile Peer to Peer |
| GPS | Global Positioning System |
| GSM | Global System for Mobile Communication |
| GPRS | General Packet Radio Service |
| TCP | Transport Control Protocol |
| LBS | Location Based Services |
| IMEI | International Mobile Equipment Identity |
| MCC | Mobile Country Code |
| MNC | Mobile Network Code |
| LAC | Location Area Code |
| CI | Cell ID |
| RSSI | Received Signal Strength Indicator |
| UDP | User Datagram Protocol |
| SOS | Save Our Ship/Save Our Souls |
| CRC | Cyclic Redundancy Check |
| NITZ | Network Identity and Time Zone, |
| GIS | Geographic Information System |

# 3. Basic rule

1．Terminal will send login information package by default and wait confirmation from the server.

2．After the normal connection is established, the terminal will regularly send GPS, LBS combined info package or GPS and LBS info package separately to server after changing of the GPS info. Server can set the default sending protocol by command.

3．To ensure the effectiveness of the connection, the terminal will send state information to server during fixed interval and the server will reply the response information package to confirm.

GT03 basic procedure:

# 4. Data package format

Communication transfer is asynchronous mode in byte. It transfers serial data stream of every uncertain length data package between terminal and server.

Data package length:（10+N）Byte

| Format | Length(Byte) |
| --- | --- |
| Start Bit | 2 |
| Packet Length | 1 |
| Protocol Number | 1 |
| Information Content | N |
| Information Serial Number | 2 |
| Error Check | 2 |
| Stop Bit | 2 |

## 4.1 Start Bit

Fixed value in HEX 0x78 0x78.

## 4.2 Package Length

Length = Protocol Number + Information Content + Information Serial Number + Error Check, totally (5+N)Bytes, because the Information Content is a variable length field.

## 4.3 Protocol number

Refer to different “information content” and correspond to the protocol number.

| Type | Value |
| --- | --- |
| Login Information package | 0x01 |
| GPS Information package | 0x10 |
| LBS Information package | 0x11 |
| Status Information package | 0x13 |
| GPS/LBS/Status Merged Information package | 0x16 |
| LBS/Checking Location Via Phone Number Information package | 0x17 |
| LBS/status merged package | 0x19 |
| GPS/Checking Location Via Phone Number Information package | 0x1A |
| Server send command to terminal (setting) | 0x80 |
| Server send command to terminal (checking) | 0x81 |

The updated protocol uses the following protocol numbers, 0X01, 0X10, 0X11, 0X13, 0X16(it is used to get GPS location information when there is SOS or vibration alarm), 0X17(it is used to get LBS location information via command DW), 0X19(it is used to get LBS location information when there is SOS or vibration alarm), 0X1A(it is used to get LBS location information via command DW), 0X80, 0X81 etc.

## 4.4 Information Contents

The specific contents are determined by the protocol numbers corresponding to different applications.

## 4.5 Information Serial Number

The serial number of the first GPRS data (including status packet and data packet such as GPS, LBS) sent after booting is ‘1’, and the serial number of data sent later at each time will be automatically added ‘1’.

## 4.6 Error Check

A check code may be used by the terminal or the server to distinguish whether the received information is error or not. To prevent errors occur during data transmission, error check is added to against data misoperation, so as to increase the security and efficiency of the system. The check code is generated by the CRC-ITU checking method.

The check codes of data in the structure of the protocol, from the Packet Length to the Information Serial Number (including “Packet Length” and “Information Serial Number”) , are values of CRC-ITU.

CRC error occur when the received information is calculated, the receiver will ignore and discard the data packet.

## 4.7 Stop Bit

Fixed value in HEX 0x0D 0x0A

# 5. Details about Data Packet sent from Terminal to Server

## 5.1 Login Message Packet

### 5.1.1 Terminal Sending Data Packet to Server

|  | Description | Bits | Example |
| --- | --- | --- | --- |
| Login Message Packet (20 Byte) | Start Bit | 2 | 0x78 0x78 |
|  | Packet Length | 1 | 0x0F |
|  | Protocol Number | 1 | 0x01 |
|  | Info content | Terminal ID | 8 | 0x01 0x23 0x45 0x67 0x89 0x01 0x23 0x45 |
|  |  | Type Identifier | 2 | 0x10 0x0B |
|  | Time zone language |  |  |
|  | Information Serial Number | 2 | 0x00 0x01 |
|  | Error Check | 2 | 0xA3 0x67 |
|  | Stop Bit | 2 | 0x0D 0x0A |

Login Information Package is used to confirm whether the connection is normal and submit terminal ID to server.

#### Start Bit

For details see Data Packet Format section 4.1.

#### Packet Length

For details see Data Packet Format section 4.2.

#### Protocol Number

For details see Data Packet Format section 4.3.

#### Terminal ID

The terminal ID applies IMEI number of 15 bits.

Example: if the IMEI is 123456789012345, the terminal ID is 0x01 0x23 0x45 0x67 0x89 0x01 0x23 0x45.

#### 5.1.1.5 Type Identifier

Type identifier occupied 2 bytes. It can be used for recognizing terminal type.

E.g.:GT03A version

Type identifier：0x10 0x0A

E.g.:GT03B version

Type identifier：0x10 0x0B

#### Time zone language

| One and a half bytes (bit15—bit4) | 15 | the 100 times of the time zone value |
| --- | --- | --- |
|  | 14 |  |
|  | 13 |  |
|  | 12 |  |
|  | 11 |  |
|  | 10 |  |
|  | 9 |  |
|  | 8 |  |
|  | 7 |  |
|  | 6 |  |
|  | 5 |  |
|  | 4 |  |
| Low half byte (bit4-bit0) | 3 | Eastern/western time zone |
|  | 2 | No current definition |
|  | 1 | Language selection bit | 1 |
|  | 0 | Language selection bit | 0 |

Bit3  0------- Eastern time zone

1------- Western time zone

e.g.：

Extension bit: 0X32 0X00, it indicates GMT+8:00.

Arithmetic: 8*100=800，convert 800 into hex value, which is 0X0320

Extension bit: 0X4D 0XD8, it indicates GMT-12:45.

Arithmetic: 12.45*100=1245, convert 1245 into hex value, which is 0X04 0XDD

Algorithmic method: to combine the time zone value with eastern/western time zone and language selection bit, so that to save the bytes.

#### Information Serial Number

For details see Data Packet Format section 4.5.

#### Error Check

For details see Data Packet Format section 4.6.

#### Stop Bit

For details see Data Packet Format section 4.7.

### 5.1.2 Server Responds the Data Packet

e.g.：

Terminal->Server（here the terminal ID is 123456789012345）

| 说明 | 位数 | 示例 |
| --- | --- | --- |
| Description | Bits | Example |
| Start Bit | 2 | 0x78 0x78 |
| Packet Length | 1 | 0x0D |
| Protocol Number | 1 | 0x01 |
| Identifier | 2 | 0x10 0x04 |
| Information Serial Number | 2 | 0x00 0x01 |
| Time zone language |  |  |
| CRC verify | 2 | 0x8C 0xDD |
| Stop Bit | 2 | 0x0D 0x0A |

//extension bit    //bit15--bit4 the 100 times of the time zone value    //bit3 Eastern/western time zone    //bit1,bit0 language (time_zone.time*100 + time_zone.time_min) <<4

Server-> Terminal：（the response protocol NO. is the same with the protocol NO. Sending by terminal）

| Description | Example |
| --- | --- |
| Start Bit | 0x78 0x78 |
| Packet Length | 0x05 |
| Protocol Number | 0x01 |
| Serial Number | 0x00 0x01 |
| CRC verify | 0xD9 0xDC |
| Stop Bit | 0x0D 0x0A |

#### Start Bit

For details see Data Packet Format section 4.1.

#### Packet Length

For details see Data Packet Format section 4.2.

#### Protocol Number

For details see Data Packet Format section 4.3.

#### Information Serial Number

For details see Data Packet Format section 4.5.

#### Error Check

For details see Data Packet Format section 4.6.

#### Stop Bit

For details see Data Packet Format section 4.7.

### 5.1.3 Function

Login message packet will be sent the first time when the terminal connects with platform, and it is used for platform to recognize different ID.

## 5.2 GPS information package（0X10）

### 5.2.1 Terminal Sending Data Packet to Server

|  | Format | Length(Byte) | Example |
| --- | --- | --- | --- |
| GPS information packet | Start Bit | 2 | 0x78 0x78 |
|  | Packet Length | 1 | 0x1F |
|  | Protocol Number | 1 | 0x10 |
|  | Information Content | Date Time | 6 | 0x0B 0x08 0x1D 0x11 0x2E 0x10 |
|  |  | GPS message length, Quantity of GPS satellites | 1 | 0x9C |
|  |  | Latitude | 4 | 0x02 0x7A 0xC7 0xEB |
|  |  | Longitude | 4 | 0x0C 0x46 0x58 0x49 |
|  |  | Speed | 1 | 0x00 |
|  |  | Course, Status | 2 | 0x14 0x8F |
|  |  | Reserved extension bit | N | 0x00 0x01 |
|  | Serial Number | 2 | 0x00 0x03 |
|  | Error Check | 2 | 0x80 0x81 |
|  | Stop Bit | 2 | 0x0D 0x0A |

#### Start Bit

For details see Data Packet Format section 4.1.

#### Packet Length

For details see Data Packet Format section 4.2.

#### Protocol Number

For details see Data Packet Format section 4.3.

#### 5.2.1.4 Date and time

| Format | Length(Byte) | Example |
| --- | --- | --- |
| Year | 1 | 0x0A |
| Month | 1 | 0x03 |
| Day | 1 | 0x17 |
| Hour | 1 | 0x0F |
| Minute | 1 | 0x32 |
| Second | 1 | 0x17 |

Example: 2010-03-23 15:30:23

Calculated as follows:	   10(Decimal)=0A(Hexadecimal)

3 (Decimal)=03(Hexadecimal)

23(Decimal)=17(Hexadecimal)

15(Decimal)=0F(Hexadecimal)

50(Decimal)=32(Hexadecimal)

23(Decimal)=17(Hexadecimal)

Then the value is: 0x0A 0x03 0x17 0x0F 0x32 0x17

#### 5.2.1.5 GPS info length/ Number of satellites involved in locating

1 byte converts to binary is 8 bit, the first 4 bit means GPS info length, the last 4 bit means number of satellite involved in locating.

Note: The length includes 1 byte occupied by itself.

For example: 0x9C means GPS information length is 9 bytes, the number of satellite involved in locating is 12.

#### 5.2.1.6 Latitude

Occupy 4 bytes, representing the latitude value. Number range is from 0 to 162000000, which represents the range form 0°to 90°.Unit: 1/500 second

Conversion method:

A Convert the latitude (degrees, minutes) data from GPS module into a new form which represents the value only in minutes;

B Multiply the converted value by 30000, and then transform the result to hexadecimal number

For example22°32.7658′,（22×60＋32.7658）×30000=40582974,then convert it to hexadecimal number 0x02 0x6B 0x3F 0x3E

#### 5.2.1.7 Longitude

Occupy 4 bytes, representing the longitude value of location data. Number ranges from 0 to 324000000, representing the range form 0°to 180°.Unit: 1/500 seconds, Conversion method is the same as latitude’s.

#### 5.2.1.8 Speed

Occupy 1 bytes, representing the speed of the terminal; ranges from 0 to 255,Unit: kilometer/hour.

#### 5.2.1.9 Status/Course

Occupy 2 bytes; representing the moving direction of the terminal; ranges from 0-360; unit: degree, regards due north as 0 degree; clockwise.

One byte is composed of eight binary. In the first byte, the first six binary represents status. The last two binary and the whole eight binary in the second byte (10 binary in total) represents course.

| BYTE_1 | Bit7 | 0 |
| --- | --- | --- |
|  | Bit6 | 0 |
|  | Bit5 | GPS real-time/differential positioning |
|  | Bit4 | GPS having been positioning or not |
|  | Bit3 | East Longitude, West Longitude |
|  | Bit2 | South Latitude, North Latitude |
|  | Bit1 | Course |
|  | Bit0 |  |
| BYTE_2 | Bit7 |  |
|  | Bit6 |  |
|  | Bit5 |  |
|  | Bit4 |  |
|  | Bit3 |  |
|  | Bit2 |  |
|  | Bit1 |  |
|  | Bit0 |  |

0：South latitude							1：North latitude

0：East longitude							1：West longitude

0：GPS has not located					1：GPS has located

0：Real time GPS						1：Different GPS

Note: The status information in the data packet is the status corresponding to the time bit recorded in the data packet.

For example: the value is 0x15 0x4C, the corresponding binary is 00010101 01001100,

BYTE_1 Bit7		0

BYTE_1 Bit6		0

BYTE_1 Bit5		0 (real time GPS)

BYTE_1 Bit4		1 (GPS has been positioned)

BYTE_1 Bit3		0 (East Longitude)

BYTE_1 Bit2		1 (North Latitude)

BYTE_1 Bit1		0

BYTE_1 Bit0		1

BYTE_2 Bit7		0

BYTE_2 Bit6		1

BYTE_2 Bit5		0				Course 332° (0101001100 in Binary, or 332 in decimal)

BYTE_2 Bit4		0

BYTE_2 Bit3		1

BYTE_2 Bit2		1

BYTE_2 Bit1		0

BYTE_2 Bit0		0

which means GPS tracking is on, real time GPS, location at north latitude, east longitude and the course is 332°.

#### 5.2.1.10 Reserved bit

Reserved bit as N is 2byte.

| BYTE_1 | Bit7 | No definition |
| --- | --- | --- |
|  | Bit6 | No definition |
|  | Bit5 | No definition |
|  | Bit4 | No definition |
|  | Bit3 | No definition |
|  | Bit2 | No definition |
|  | Bit1 | No definition |
|  | Bit0 | No definition |
| BYTE_2 | Bit7 | No definition |
|  | Bit6 | No definition |
|  | Bit5 | No definition |
|  | Bit4 | No definition |
|  | Bit3 | No definition |
|  | Bit2 | No definition |
|  | Bit1 | Language selection bit 1 |
|  | Bit0 | Language selection bit 2 |

Note:

Language selection bit 0=1 (or 0), language selection bit 1=0, means the txt message ask platform to reply Chinese location information.

Language selection bit 0=1, language selection bit 1=1, means txt message ask platform to reply English location information.

E.g.: Extension bit value is 0x00 0x00 or 0x00 0x01, that means ask for Chinese location information. Value is 0x00 0x02 means English one.

#### Information Serial Number

For details see Data Packet Format section 4.5.

#### Error Check

For details see Data Packet Format section 4.6.

#### Stop Bit

For details see Data Packet Format section 4.7.

### 5.2.2 Server response

The server needs to response after receiving the data packet.

|  | Format | Length(Byte) | Example |
| --- | --- | --- | --- |
| Server response（10 Byte） | Start Bit | 2 | 0x78 0x78 |
|  | Data Bit Length | 1 | 0x05 |
|  | Protocol Number | 1 | 0x10 |
|  | Serial Number | 2 | 0x00 0x01 |
|  | Error Check | 2 | 0xD9 0xDC |
|  | Stop Bit | 2 | 0x0D 0x0A |

#### Start Bit

For details see Data Packet Format section 4.1.

#### Packet Length

For details see Data Packet Format section 4.2.

#### Protocol Number

For details see Data Packet Format section 4.3.

#### Information Serial Number

For details see Data Packet Format section 4.5.

#### Error Check

For details see Data Packet Format section 4.6.

#### Stop Bit

For details see Data Packet Format section 4.7.

### 5.2.3 Function

The terminal will upload GPS location after connected with platform and located by GPS.

If the GPS need work for long time, such as SOS active GPS or active GPS on platform, GPS will work for 20mins. At this moment, GPS will upload location data for every 10s by default. If the terminal does not support GPS work for long time, this data package will not be uploaded.

5.2.4 Example

Upload：0x78 0x78 0x19 0x10 0x 0x0B 0x03 0x1A 0x0B 0x1B 0x31 0xCC 0x02 0x7A 0xC7 0xFD 0x0C 0x46 0x57 0xBF 0x01 0x15 0x21 0x00 0x01 0x00 0x1C 0xC6 0x07 0x0D 0x0A
Receive：0x78 0x78 0x05 0x10 0x00 0x1D 0xDC 0x78 0x0D 0x0A

## 5.3 LBS information package (0x11)

### 5.3.1 Terminal Sending Data Packet to Server

| Format | Length (Byte) | Example |
| --- | --- | --- |
| Start Bit | 2 | 0x78 0x78 |
| Packet Length | 1 | 0x15 |
| Protocol Number | 1 | 0x11 |
| Info content | Date Time | 6 | 0x00 0x00 0x00 0x00 0x00 0x00 |
|  | LBS Information | MCC | 2 | 0x01 0xCC |
|  |  | MNC | 1 | 0x00 |
|  |  | LAC | 2 | 0x26 0x6A |
|  |  | Cell ID | 3 | 0x00 0x1D 0xF1 |
|  | Reserved extension bit | N | 0x00 0x01 |
| Serial Number | 2 | 0x00 0x18 |
| Error Check | 2 | 0x91 0x88 |
| Stop Bit | 2 | 0x0D 0x0A |

#### Start Bit

For details see Data Packet Format section 4.1.

#### Packet Length

For details see Data Packet Format section 4.2.

#### Protocol Number

For details see Data Packet Format section 4.3.

#### 5.3.1.4 Data and time

The same format as GPS info content mentioned before.

#### 5.3.1.5 MCC

Affiliated country code of mobile user is Mobile Country Code (MCC). MMC of China is 460(decimal).

Value ranges：0x0000 ～ 0x03E7

MMC of China：0x01 0xCC(460 decimal convert to hex)

#### 5.3.1.6 MNC

Mobile Network Code(MNC)，for example China Mobile Network Code (MNC) is 0x00.

#### 5.3.1.7 LAC

Location Area Code (LAC) is included in LAI. It is composed of 2 bytes with hex code, ranges from 0x0001－0xFFFE(not include 0x0001 and 0xFFFE). One location area can contain one or more areas.

#### 5.3.1.8 CI（Cell ID）

Cell ID (Cell ID) ranges from 0x000000 to 0xFFFFFF

#### 5.3.1.9 Reserved extension bit

Reserved bit is 2 byte, the same as GPS data package definitions.

#### Information Serial Number

For details see Data Packet Format section 4.5.

#### Error Check

For details see Data Packet Format section 4.6.

#### Stop Bit

For details see Data Packet Format section 4.7.

### 5.3.2 Server response

The server needs to response after receiving the data packet.

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Server response（10 Byte） | Start Bit | 2 | 0x78 0x78 |
|  | Data Bit Length | 1 | 0x05 |
|  | Protocol Number | 1 | 0x11 |
|  | Serial Number | 2 | 0x00 0x01 |
|  | Error Check | 2 | 0xD9 0xDC |
|  | Stop Bit | 2 | 0x0D 0x0A |

#### Start Bit

For details see Data Packet Format section 4.1.

#### Packet Length

For details see Data Packet Format section 4.2.

#### Protocol Number

For details see Data Packet Format section 4.3.

#### Information Serial Number

For details see Data Packet Format section 4.5.

#### Error Check

For details see Data Packet Format section 4.6.

#### Stop Bit

For details see Data Packet Format section 4.7.

### 5.3.3 Function

The terminal starts to upload LBS data package after connected with platform.

The terminal will upload LBS data package every 2mins by default.

### 5.3.4 Example

Upload：0x78 0x78 0x15 0x11 0x00 0x00 0x00 0x00 0x00 0x00 0x01 0xCC 0x00 0x26 0x6A 0x00 0x1D 0xF1 0x00 0x01 0x00 0x18 0x91 0x88 0x0D 0x0A

Receive：0x78 0x78 0x05 0x11 0x00 0x18 0xD1 0x09 0x0D 0x0A

## 5.4 Status info package (0x13)

### 5.4.1 Terminal Sending Status info Packet to Server

| Format | Length (Byte) | Example |
| --- | --- | --- |
| Start Bit | 2 | 0x78 0x78 |
| Packet Length | 1 | 0x0A |
| Protocol Number | 1 | 0x13 |
| Information Content | Terminal Information | 1 | 0x40 |
|  | Voltage Level | 1 | 0x06 |
|  | GSM Signal Strength | 1 | 0x04 |
|  | Reserved extension bit | N | 0x00 0x01 |
| Serial Number | 2 | 0x00 0x1F |
| Error Check | 2 | 0xC4 0x39 |
| Stop Bit | 2 | 0x0D 0x0A |

#### 5.4.1.1 Start Bit

For details see Data Packet Format section 4.1.

#### Packet Length

For details see Data Packet Format section 4.2.

#### Protocol Number

For details see Data Packet Format section 4.3.

#### 5.4.1.4 Terminal Information

One byte is consumed defining for various status information of the mobile phone.

1 byte is regarded as 8 bit, the lowest bit is 0 bit, and the highest bit is 7 bit, when transferring, the higher bit has priority. Each bit meaning is as follow:

| High |  |  |  |  |  |  | Low |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |

| Bit | Code Meaning |
| --- | --- |
| BYTE | Bit7 | No definition |
|  | Bit6 | 1: GPS tracking is on |
|  |  | 0: GPS tracking is off |
|  | Bit3~ Bit5 | 110: out of fence |
|  |  | 101: enter fence |
|  |  | 100: SOS |
|  |  | 011: Low Battery Alarm |
|  |  | 001: Shock Alarm |
|  |  | 000: Normal |
|  | Bit2 | 1: Charge On |
|  |  | 0: Charge Off |
|  | Bit1 | 1: ACC high |
|  |  | 0: ACC Low |
|  | Bit0 | 1: Activated |
|  |  | 0: Deactivated |

Note: All status info in data packages are the status recorded by time bit at that moment in the data package.

#### 5.4.1.5 Voltage Level

The range is 0~6 defining the voltage is from low to high.

0: No Power (shutdown)

1: Extremely Low Battery (not enough for calling or sending text messages, etc.)

2: Very Low Battery (Low Battery Alarm)

3: Low Battery (can be used normally)

4: Medium

5: High

6: Very High

#### GSM Signal Strength Levels

0x00: no signal;

0x01: extremely weak signal;

0x02: very weak signal;

0x03: good signal;

0x04: strong signal.

#### 5.4.1.7 Reserved extension bit

Reserved bit is 2 bytes and the same as GPS data package definition.

#### Information Serial Number

For details see Data Packet Format section 4.5.

#### Error Check

For details see Data Packet Format section 4.6.

#### Stop Bit

For details see Data Packet Format section 4.7

### 5.4.2 Server response

The server needs to response after receiving the data packet.

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Server response（10 Byte） | Start Bit | 2 | 0x78 0x78 |
|  | Data Bit Length | 1 | 0x05 |
|  | Protocol Number | 1 | 0x13 |
|  | Serial Number | 2 | 0x00 0x01 |
|  | Error Check | 2 | 0xD9 0xDC |
|  | Stop Bit | 2 | 0x0D 0x0A |

#### Start Bit

For details see Data Packet Format section 4.1.

#### Packet Length

For details see Data Packet Format section 4.2.

#### Protocol Number

For details see Data Packet Format section 4.3.

#### Information Serial Number

For details see Data Packet Format section 4.5.

#### Error Check

For details see Data Packet Format section 4.6.

#### Stop Bit

For details see Data Packet Format section 4.7.

### 5.4.3 Functions

The terminal starts to upload terminal status of battery energy and so on after connected with platform.

The terminal will upload status data package every 5mins by default.

### 5.4.4 Example

Send：0x78 0x78 0x0A 0x13 0x40 0x06 0x04 0x00 0x01 0x00 0x1F 0xC4 0x39 0x0D 0x0A

Receive 0x78 0x78 0x05 0x13 0x00 0x1F 0x10 0x0E 0x0D 0x0A

## 5.5 Combined information packet of GPS, LBS and Status (0X16)

### 5.5.1 Terminal Sending Data Packet to Server

| Format | Length (Byte) | Example |
| --- | --- | --- |
| Start Bit | 2 | 0x78 0x78 |
| Packet Length | 1 | 0x0A |
| Protocol Number | 1 | 0x16 |
| Information Content | Date Time | 6 | 0x0B 0x08 0x1D 0x11 0x2E 0x10 |
|  | GPS Information | GPS information length, Quantity of GPS information satellites | 1 | 0x9C |
|  |  | Latitude | 4 | 0x02 0x7A 0xC7 0xEB |
|  |  | Longitude | 4 | 0x0C 0x46 0x58 0x49 |
|  |  | Speed | 1 | 0x00 |
|  |  | Course, Status | 2 | 0x14 0x8F |
|  |  | Reserved extension bit | M |  |
|  | LBS Information | LBS Length | 1 | 0x08 |
|  |  | MCC | 2 | 0x01 0xCC |
|  |  | MNC | 1 | 0x00 |
|  |  | LAC | 2 | 0x26 0x6A |
|  |  | Cell ID | 3 | 0x00 0x1D 0xF1 |
|  |  | Reserved extension bit | N |  |
|  | status Information | Terminal Information Content | 1 | 0x40 |
|  |  | Voltage Level | 1 | 0x06 |
|  |  | GSM Signal Strength | 1 | 0x04 |
| Serial Number | 2 | 0x00 0x1F |
| Error Check | 2 | 0xC4 0x39 |
| Stop Bit | 2 | 0x0D 0x0A |

#### Start Bit

For details see Data Packet Format section 4.1.

#### Packet Length

For details see Data Packet Format section 4.2.

#### Protocol Number

For details see Data Packet Format section 4.3.

#### 5.5.1.4 Information content

We have integrated the status info package based on GPS, LBS info package.

Note: the length of this LBS info has been enlarged (including 1 Byte occupied by the length itself)）, the server must make corresponding response after received “GPS, status combined info” package.

Reserved extension bit M=0; Reserved extension bit N=0;

#### Information Serial Number

For details see Data Packet Format section 4.5.

#### Error Check

For details see Data Packet Format section 4.6.

#### Stop Bit

For details see Data Packet Format section 4.7.

### 5.5.2 Server response

The terminal asks server for replying Chinese or English address, the replying data packages are different according to extension command.

Replying data package of Chinese:

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Command packet sent from the server to the terminal （15+M Byte） | Start Bit | 2 | 0x78 0x78 |
|  | Packet length | 1 | 0x84 |
|  | Protocol Number | 1 | 0x16 |
|  | Information Content | Length of Command | 1 | 0x7E |
|  |  | Server Flag Bit | 4 | 0x00 0x00 0x00 0x01 |
|  |  | Command content | M |  |
|  |  | Reserved extension bit | 0 |  |
|  | Information Serial Number | 2 | 0x00 0x01 |
|  | Check Bit | 2 | 0xD9 0xDC |
|  | Stop Bit | 2 | 0x0D 0x0A |

Applying Chinese address protocol no.:0X16.

Info content is as below：

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Information Content | Length of Command | 1 | 0x7E |
|  | Server Flag Bit | 4 | 0x00 0x00 0x00 0x01 |
|  | Command content | M |  |
|  | Reserved extension bit | 0 |  |

Command content: ADDRESS&&address content&&phone number##

Chinese address content will be sent as Unicode.

Regarding the foreign countries’addresses information are longer; add data bit into 2 Bytes in case of 1 data is not enough.

Note：

Only the data bit length of address info protocol No. is changed into 2 Bytes.

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Command packet sent from the server to the terminal （17+M Byte） | Start Bit | 2 | 0x78 0x78 |
|  | Packet length | 2 | 0x00 0xD1 |
|  | Protocol Number | 1 | 0x96 |
|  | Information Content | Length of Command | 2 | 0x00 0xCA |
|  |  | Server Flag Bit | 4 | 0x00 0x00 0x00 0x01 |
|  |  | Command content | M |  |
|  |  | Reserved extension bit | 0 |  |
|  | Information Serial Number | Information Serial Number | 0x00 0x07 |
|  | Check Bit | Check Bit | 0x72 0xb5 |
|  | Stop Bit | Stop Bit | 0x0D 0x0A |

Applying for English address protocol: 0X96

### 5.5.3 Functions

The terminal will send this status package to server, including terminal alarm status and apply for address information when SOS is calling under the condition that GPS has already located.

## 5.6 LBS, phone number checking location info package (0X17)

### 5.6.1 Terminal Sending Data Packet to Server

| Format | Length (Byte) | Example |
| --- | --- | --- |
| Start Bit | 2 | 0x78 0x78 |
| Packet Length | 1 | 0x1F |
| Protocol Number | 1 | 0x17 |
| Info content | LBS info | MCC | 2 | 0x01 0xCC |
|  |  | MNC | 1 | 0x00 |
|  |  | LAC | 2 | 0x26 0x6A |
|  |  | Cell ID | 3 | 0x00 0x1D 0xF1 |
|  | Phone number | 21 |  |
|  | Reserved extension bit | N |  |
| Serial Number | 2 | 0x00 0x03 |
| Check Bit | 2 | 0x80 0x81 |
| Stop Bit | 2 | 0x0D 0x0A |

#### Start Bit

For details see Data Packet Format section 4.1.

#### Packet Length

For details see Data Packet Format section 4.2.

#### Protocol Number

For details see Data Packet Format section 4.3.

#### 5.6.1.4 Information content

The format is almost the same as the one mentioned in LBS info content, just reduce an item of date and time and add an item of checking address by phone number.

Note: Reserved extension bit N=0.

#### Information Serial Number

For details see Data Packet Format section 4.5.

#### Error Check

For details see Data Packet Format section 4.6.

#### Stop Bit

For details see Data Packet Format section 4.7.

### 5.6.2 Server response

The server replies Chinese address or English address based on the extended command, and the response data packet is inconsistent

The response data packet in Chinese is as follow:

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Command packet sent from the server to the terminal （15+M Byte） | Start Bit | 2 | 0x78 0x78 |
|  | Packet Length | 1 | 0x05 |
|  | Protocol Number | 1 | 0x17 |
|  | Information Content | Length of Command | 1 | 0x7E |
|  |  | Server Flag Bit | 4 | 0x00 0x00 0x00 0x01 |
|  |  | Command content | M |  |
|  |  | Reserved extension bit | 0 |  |
|  | Information Serial Number | 2 | 0x00 0x01 |
|  | Check Bit | 2 | 0xD9 0xDC |
|  | Stop Bit | 2 | 0x0D 0x0A |

The Protocol Number of request Chinese address response is 0X17.

Info content is as below:

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Information Content | Length of Command | 1 | 0x7E |
|  | Server Flag Bit | 4 | 0x00 0x00 0x00 0x01 |
|  | Command content | M |  |
|  | Reserved extension bit | 0 |  |

Command Content: ADDRESS&&Address Content&&Phone Number##

Chinese address content is sent in UNICODE.

Considering the address or other foreign address in English is generally longer than that in Chinese, one data bit is not enough, so the data bit is occupied in 2 bytes.

Note: only the packet length corresponding to the protocol number of response address information is changed into two bytes.

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Command packet sent from the server to the terminal（17+M Byte） | Start Bit | 2 | 0x78 0x78 |
|  | Packet length | 2 | 0x00 0xD1 |
|  | Protocol Number | 1 | 0x97 |
|  | Information Content | Length of Command | 2 | 0x00 0xCA |
|  |  | Server Flag Bit | 4 | 0x00 0x00 0x00 0x01 |
|  |  | Command content | M |  |
|  |  | Reserved extension bit | 0 |  |
|  | Information Serial Number | 2 | 0x00 0x01 |
|  | Check Bit | 2 | 0xD9 0xDC |
|  | Stop Bit | 2 | 0x0D 0x0A |

The Protocol Number of request English address response is 0X97.

### 5.6.3 Functions

The terminal will send this status package to ask terminal address info when SMS command DW is sent.

### 5.6.4 Example

A. Example of Chinese address response information:

7878            //start bit

84              // data length

17              // Response Protocol Number

7E              //command length, i.e.: SMS content length

00000001        //serial number sent from server

41444452455353  //ADDRESS

2626            //&& separator

624059044F4D7F6E0028    // Chinese address is sent in UNICODE

004C004200530029003A

5E7F4E1C77015E7F5DDE

5E0282B190FD533AFF17

FF15FF144E6190530028

004E00320033002E0033

00390035002C00450031

00310032002E00390038

0038002996448FD1

2626             //&& separator

313337313038313931333500000000000000000000     //phone number

2323             //## terminator of content

0106             // Serial No.

3825             // Check Bit

0D0A             //end bit

B. Example of English address info replying：

7878       //start bit

00D1       //data length

97         // Response Protocol Number

00CA       //command length; content info length;

00000001    //serial number sent from server

41444452455353   //ADDRESS

2626            //&& separator

0053004F00530028004C    // English address is sent in UNICODE

0029003A005300680069

006D0069006E00200046

0061006900720079006C

0061006E006400200057

00650073007400200052

0064002C004800750069

006300680065006E0067

002C004800750069007A

0068006F0075002C0047

00750061006E00670064

006F006E00670028004E

00320033002E00310031

0031002C004500310031

0034002E003400310031

0029004E006500610072

00620079

2626                 //&& separator

313235323031333739303737343035310000000000     //phone number

2323            //## terminator of content

0007            //serial number

72b5            //check bit

0D0A            //end bit

## LBS Extension Info Package (0X18)

| Format | Length (Byte) |
| --- | --- |
| Information Content | Date &Time | 6 |
|  | LBS info | MCC | 2 |
|  |  | MNC | 1 |
|  |  | LAC | 2 |
|  |  | CI | 2 |
|  |  | RSSI | 1 |
|  |  | NLAC1 | 2 |
|  |  | NCI1 | 2 |
|  |  | NRSSI1 | 1 |
|  |  | NLAC2 | 2 |
|  |  | NCI2 | 2 |
|  |  | NRSSI2 | 1 |
|  |  | NLAC3 | 2 |
|  |  | NCI3 | 2 |
|  |  | NRSSI3 | 1 |
|  |  | NLAC4 | 2 |
|  |  | NCI4 | 2 |
|  |  | NRSSI4 | 1 |
|  |  | NLAC5 | 2 |
|  |  | NCI5 | 2 |
|  |  | NRSSI5 | 1 |
|  |  | NLAC6 | 2 |
|  |  | NCI6 | 2 |
|  |  | NRSSI6 | 1 |
|  | Reserved bit | N |

### Terminal Sending Data Packet to Server

#### Date &Time

Same as the description of last section

#### MCC

Same as the description of last section

#### MNC

Same as the description of last section

#### LAC

Same as the description of last section

#### CI（Cell ID）

Cell ID, the value range is 0x0000 ～ 0xFFFF。

#### RSSI（Received Signal Strength Indicator）

Received Signal Strength Indicator, the value range is 0x00～0xFF，0x00 signal is the weakest, 0xFF is strongest.

#### NLAC1～6

#### Neighboring received location codes, 6 in total.

#### NCI1～6（Neighboring Cell ID）

Neighboring Cell ID, which are corresponded with 6 NLAC.

#### NRSSI1～6（Near Cell ID Signal Strength）

Near Cell ID Signal Strength, which are corresponded with 6 NLAC.

## 5.8 LBS, Status info package（0X19）

### 5.8.1 Terminal Sending Data Packet to Server

| Format | Length (Byte) | Example |
| --- | --- | --- |
| Start Bit | 2 | 0x78 0x78 |
| Packet Length | 1 | 0x15 |
| Protocol Number | 1 | 0x19 |
| Information Content | LBS Information | MCC | 2 | 0x01 0xCC |
|  |  | MNC | 1 | 0x00 |
|  |  | LAC | 2 | 0x26 0x6A |
|  |  | Cell ID | 3 | 0x00 0x1D 0xF1 |
|  | Status Information | Terminal Information Content | 1 | 0x40 |
|  |  | Voltage Level | 1 | 0x06 |
|  |  | GSM Signal Strength | 1 | 0x04 |
| Serial Number | 2 | 0x00 0x1F |
| Error Check | 2 | 0xC4 0x39 |
| Stop Bit | 2 | 0x0D 0x0A |

#### Start Bit

For details see Data Packet Format section 4.1.

#### Packet Length

For details see Data Packet Format section 4.2.

#### Protocol Number

For details see Data Packet Format section 4.3.

#### Information Content

Almost the same as ones mentioned in LBS info content above.

#### Information Serial Number

For details see Data Packet Format section 4.5.

#### Error Check

For details see Data Packet Format section 4.6.

#### Stop Bit

For details see Data Packet Format section 4.7.

### 5.8.2 Server response

The server needs to response after receiving the data packet.

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Server response（10 Byte） | Start Bit | 2 | 0x78 0x78 |
|  | Packet length | 1 | 0x05 |
|  | Protocol Number | 1 | 0x19 |
|  | Information Serial Number | 2 | 0x00 0x01 |
|  | Check Bit | 2 | 0xD9 0xDC |
|  | Stop Bit | 2 | 0x0D 0x0A |

#### 5.8.2.1 Start Bit

For details see Data Packet Format section 4.1.

#### 5.8.2.2 Packet Length

For details see Data Packet Format section 4.2.

#### 5.8.2.3Protocol Number

For details see Data Packet Format section 4.3.

#### 5.8.2.4Information Serial Number

For details see Data Packet Format section 4.5.

#### 5.8.2.5Error Check

For details see Data Packet Format section 4.6.

#### 5.8.2.6Stop Bit

For details see Data Packet Format section 4.7.

### 5.8.3 Functions

After terminal and platform are connected, press SOS key to send this data package, send terminal alarm status and apply for LBS location info to server.

## 5.9 GPS, phone number checking location info package (0X1A)

### 5.9.1 Terminal Sending Data Packet to Server

| Format | Length (Byte) | Example |
| --- | --- | --- |
| Start Bit | 2 | 0x78 0x78 |
| Packet Length | 1 | 0x1F |
| Protocol Number | 1 | 0x1A |
| Information Content | Date Time | 6 | 0x0B 0x08 0x1D 0x11 0x2E 0x10 |
|  | GPS Information | Length of GPS information, quantity of positioning satellites | 1 | 0xCF |
|  |  | Latitude | 4 | 0x02 0x7A 0xC7 0xEB |
|  |  | Longitude | 4 | 0x0C 0x46 0x58 0x49 |
|  |  | Speed | 1 | 0x00 |
|  |  | Course, Status | 2 | 0x14 0x8F |
|  | Phone Number | 21 |  |
|  | Reserved extension bit | N |  |
| Information Serial Number | 2 | 0x00 0x03 |
| Error Check | 2 | 0x80 0x81 |
| Stop Bit | 2 | 0x0D 0x0A |

#### 5.9.1.1 Start Bit

For details see Data Packet Format section 4.1.

#### 5.9.1.2 Packet Length

For details see Data Packet Format section 4.2.

#### 5.9.1.3 Protocol Number

For details see Data Packet Format section 4.3.

#### 5.9.1.4 Information Content

Almost the same as ones mentioned in GPS info content above, while adding an item of checking location by phone number.

#### 5.9.1.5 Information Serial Number

For details see Data Packet Format section 4.5.

#### 5.9.1.6 Error Check

For details see Data Packet Format section 4.6.

#### 5.9.1.7 Stop Bit

For details see Data Packet Format section 4.7.

### 5.9.2 Server response

The server replies Chinese address or English address based on the extended command, and the response data packet is inconsistent

The response data packet in Chinese is as follow:

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Command packet sent from the server to the terminal (15+M+N Byte) | Start Bit | 2 | 0x78 0x78 |
|  | Length of data bit | 1 | 0x0F |
|  | Protocol Number | 1 | 0x1A |
|  | Information Content | Length of Command | 1 | 0x7E |
|  |  | Server Flag Bit | 4 | 0x00 0x00 0x00 0x01 |
|  |  | Command content | M |  |
|  |  | Reserved extension bit | 0 |  |
|  | Information Serial Number | 2 | 0x00 0x01 |
|  | Check Bit | 2 | 0xD9 0xDC |
|  | Stop Bit | 2 | 0x0D 0x0A |

The Protocol Number of request Chinese address response is 0X17.

#### Info content is as below:

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Information Content | Length of Command | 1 | 0x7E |
|  | Server Flag Bit | 4 | 0x00 0x00 0x00 0x01 |
|  | Command content | M |  |
|  | Reserved extension bit | 0 |  |

Command Content: ADDRESS&&Address Content&&Phone Number##

Chinese address content is sent in UNICODE.

Considering the address or other foreign address in English is generally longer than that in Chinese, one data bit is not enough, so the data bit is occupied in 2 bytes.

Note: only the length of data bit corresponding to the protocol number of response address information is changed into two bytes.

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Command packet sent from the server to the terminal（17+M Byte） | Start Bit | 2 | 0x78 0x78 |
|  | Length of data bit | 2 | 0x05 |
|  | Protocol Number | 1 | 0x9A |
|  | Information Content | Length of Command | 2 | 0x00 0xCA |
|  |  | Server Flag Bit | 4 | 0x00 0x00 0x00 0x01 |
|  |  | Command content | M |  |
|  |  | Reserved extension bit | 0 |  |
|  | Information Serial Number | Information Serial Number | 0x00 0x01 |
|  | Check Bit | Check Bit | 0xD9 0xDC |
|  | Stop Bit | Stop Bit | 0x0D 0x0A |

The Protocol Number of request English address response is 0X97.

### 5.9.3 Functions

The server will send this data package while sending txt message command to activate GPS and apply for location info.

# 6. Data Packet Sent From Server to Terminal

## 6.1 Command from server to terminal（Setting Command 0X80）

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Command packet sent from the server to the terminal（15+M Byte） | Start Bit | 2 | 0x78 0x78 |
|  | Packet length | 1 | 0x0F |
|  | Protocol Number | 1 | 0x80 |
|  | Information Content | Length of Command | 1 | 0x00 0xCA |
|  |  | Server Flag Bit | 4 | 0x00 0x00 0x00 0x01 |
|  |  | Command content | M |  |
|  |  | Reserved extension bit | 0 |  |
|  | Information Serial Number | 2 | 0x00 0x01 |
|  | Error Check | 2 | 0xD9 0xDC |
|  | Stop Bit | 2 | 0x0D 0x0A |

The Protocol Number is 0x80.

The terminal response the command from server，data package format is the same as the command format from server to terminal. The protocol no. is different, using “0x80” or “0x81”. 0x80 is setting command, 0x81 is checking command.

Note：Reserved extension bit N=0;

#### Start Bit

For details see Data Packet Format section 4.1.

#### Packet Length

For details see Data Packet Format section 4.2.

#### Protocol Number

For details see Data Packet Format section 4.3.

#### Length of Command

Measured in bytes, 0x0A means the content of command occupied ten bytes.

#### Server Flag Bit

It is reserved to the identification of the server. The binary data received by the terminal is returned without change.

#### Command Content

It is represented in ASC II of string, and the command content is compatible with text message command.

#### 6.1.6.1 Activate GPS online

SMS command format:

GPSON#

Function description：Start GPS locating function

Returned SMS:

If successful, return：GPSON=Success!

If failed, return：GPSON=Fail!

#### Set SOS numbers online

SMS command format:

SOS, Operate symbol (A), Number 1, Number 2, Number 3, Number 4#

e.g.：

SOS,A,13790774051,13790774051,13790774051,13790774051#

Function description: Set sos numbers

Returned SMS:

If successful, return：SOS=Success!

If failed, return：SOS=Fail!

e.g.：

SOS ,A,13790774051,13553442881,13556286698,13525449308#（add 4 numbers at one time）

SOS,A,13790774051#（add the first SOS number）

SOS,A, ,13553442881#（add the second SOS number）

SOS,A, , ,13556286698 #（add the third SOS number）

SOS,A, , , ,13525449308#（add the fourth SOS number）

SOS,A,13790774051, 13553442881#(add the first and second SOS number)

SOS,A,13790774051, 13553442881, 13556286698#( add the first, second and third SOS number)

#### Reserved extension bit

Currently, the Reserved extension bit sent from server to terminal is N=0.

#### Information Serial Number

For details see Data Packet Format section 4.5.

#### Error Check

For details see Data Packet Format section 4.6.

#### Stop Bit

For details see Data Packet Format section 4.7.

6.1.11 Example

A. Example of activate GPS online:

7878   //start bit

10    // data packet length

80     // protocol number

0A     //content length

0000A039  //serial number from server

4750534F4E  //GPSON

23        //#

0001    //serial number

238     //CRC check

d0D0A   //end

B. Example of set SOS online:

7878   //Start bit

2A    //data package length

80     // protocol number

24     // content length

00009F5D  //serial number from server

534F53   //SOS

2C       //,

41        //A

2C        //,

3133303534383732383039  //13054872809

2C   //,

2C   //,

2C   //,

3133373036343132363334  //13706412634

23       //#

0001    //serial number

c6ba    //CRC check

0D0A    //end

## 6.2 Command sent from server to terminal（checking command 0X81）

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Command packet sent from the server to the terminal（15+M Byte） | Start Bit | 2 | 0x78 0x78 |
|  | Packet length | 1 | 0x0F |
|  | Protocol Number | 1 | 0x81 |
|  | Information Content | Length of Command | 1 | 0x00 0xCA |
|  |  | Server Flag Bit | 4 | 0x00 0x00 0x00 0x01 |
|  |  | Command content | M |  |
|  |  | Reserved extension bit | 0 |  |
|  | Information Serial Number | 2 | 0x00 0x01 |
|  | Error Check | 2 | 0xD9 0xDC |
|  | Stop Bit | 2 | 0x0D 0x0A |

Protocol number：0x81，Reserved extension bit N=0;

#### Start Bit

For details see Data Packet Format section 4.1.

#### Packet Length

For details see Data Packet Format section 4.2.

#### Protocol Number

For details see Data Packet Format section 4.3.

#### Length of Command

Measured in bytes, 0x0A means the content of command occupied ten bytes.

#### Server Flag Bit

It is reserved to the identification of the server. The binary data received by the terminal is returned without change.

#### Command Content

It is represented in ASC II of string, and the command content is compatible with text message command.

#### 6.2.6.1 Check SOS number online

SMS command format：SEESOS#

Function description：check SOS number online

Return information：

Return info if SOS numbers are set:

SEESOS,13790774051,13553442881,13556286698.15917750508#

Return info if no SOS number is set:   SEESOS:,,,#

Return info if only one SOS number is set:  SEESOS:13790774051,,,#

Return info if two SOS numbers are set:  SEESOS:13790774051,13553442881,,#

Return info of checking is as above, if the current SOS number is blank, please use comma to separate.

#### Reserved extension bit

Currently the reserved extension bit sent from server is N=0.

#### Information Serial Number

For details see Data Packet Format section 4.5.

#### Error Check

For details see Data Packet Format section 4.6.

#### Stop Bit

For details see Data Packet Format section 4.7.

# 7. Instruction about login data package and status package

  - If a GPRS connection is established successfully, the terminal will send a first login message packet to the server and, within five seconds, if the terminal receives a data packet responded by the server, the connection is considered to be a normal connection. The terminal will begin to send location information (i.e., GPS, LBS information package). A status information package will be sent by the terminal after three minutes to regularly confirm the connection.

  - If the GPRS connection is established unsuccessfully, the terminal will not be able to send the login message packet. The terminal will start schedule reboot in twenty minutes if the GPRS connection is failed three times. Within twenty minutes, if the terminal successfully connects to the server and receives the data packet from the server as the server’s response to the login message packet sent by the terminal, the schedule reboot will be off and the terminal will not be rebooted; otherwise, the terminal will be rebooted automatically in twenty minutes.

  - After receiving the login message packet, the server will return a response data packet. If the terminal doesn’t receive packet from the server within five seconds after sending the login message packet or the status information package, the current connection is regarded as an abnormal connection. The terminal will start a retransmission function for GPS tracking data, which will cause the terminal to disconnect the current GPRS connection, rebuild a new GPRS connection and send a login message packet again.

  - If the connection is regarded to be abnormal, and the data packet as a response from the server is failed to be received three times after a connection is established and a login message packet or status information package is sent, the terminal will start schedule reboot and the scheduled time is ten minutes. Within ten minutes, if the terminal successfully connects to the server and receives the data packet responded by the server, the schedule reboot will be off and the terminal will not be rebooted; otherwise, the terminal will be rebooted automatically in ten minutes.

  - Server will not return data package to terminal which has not been registered. The connection will be ended directly.

  - When SIM card is not inserted, the GRPS connection will not be activated, and the terminal will not restart automatically.

When SIM cars is inserted while the GPRS connection is not on, the terminal will restart automatically after 20 minutes.

# 8. Appendix A: code fragment of the CRC-ITU lookup table algorithm implemented based on C language

Code fragment of the CRC-ITU lookup table algorithm implemented based on C language is as follow:

static const U16 crctab16[] =

{

0X0000, 0X1189, 0X2312, 0X329B, 0X4624, 0X57AD, 0X6536, 0X74BF,

0X8C48, 0X9DC1, 0XAF5A, 0XBED3, 0XCA6C, 0XDBE5, 0XE97E, 0XF8F7,

0X1081, 0X0108, 0X3393, 0X221A, 0X56A5, 0X472C, 0X75B7, 0X643E,

0X9CC9, 0X8D40, 0XBFDB, 0XAE52, 0XDAED, 0XCB64, 0XF9FF, 0XE876,

0X2102, 0X308B, 0X0210, 0X1399, 0X6726, 0X76AF, 0X4434, 0X55BD,

0XAD4A, 0XBCC3, 0X8E58, 0X9FD1, 0XEB6E, 0XFAE7, 0XC87C, 0XD9F5,

0X3183, 0X200A, 0X1291, 0X0318, 0X77A7, 0X662E, 0X54B5, 0X453C,

0XBDCB, 0XAC42, 0X9ED9, 0X8F50, 0XFBEF, 0XEA66, 0XD8FD, 0XC974,

0X4204, 0X538D, 0X6116, 0X709F, 0X0420, 0X15A9, 0X2732, 0X36BB,

0XCE4C, 0XDFC5, 0XED5E, 0XFCD7, 0X8868, 0X99E1, 0XAB7A, 0XBAF3,

0X5285, 0X430C, 0X7197, 0X601E, 0X14A1, 0X0528, 0X37B3, 0X263A,

0XDECD, 0XCF44, 0XFDDF, 0XEC56, 0X98E9, 0X8960, 0XBBFB, 0XAA72,

0X6306, 0X728F, 0X4014, 0X519D, 0X2522, 0X34AB, 0X0630, 0X17B9,

0XEF4E, 0XFEC7, 0XCC5C, 0XDDD5, 0XA96A, 0XB8E3, 0X8A78, 0X9BF1,

0X7387, 0X620E, 0X5095, 0X411C, 0X35A3, 0X242A, 0X16B1, 0X0738,

0XFFCF, 0XEE46, 0XDCDD, 0XCD54, 0XB9EB, 0XA862, 0X9AF9, 0X8B70,

0X8408, 0X9581, 0XA71A, 0XB693, 0XC22C, 0XD3A5, 0XE13E, 0XF0B7,

0X0840, 0X19C9, 0X2B52, 0X3ADB, 0X4E64, 0X5FED, 0X6D76, 0X7CFF,

0X9489, 0X8500, 0XB79B, 0XA612, 0XD2AD, 0XC324, 0XF1BF, 0XE036,

0X18C1, 0X0948, 0X3BD3, 0X2A5A, 0X5EE5, 0X4F6C, 0X7DF7, 0X6C7E,

0XA50A, 0XB483, 0X8618, 0X9791, 0XE32E, 0XF2A7, 0XC03C, 0XD1B5,

0X2942, 0X38CB, 0X0A50, 0X1BD9, 0X6F66, 0X7EEF, 0X4C74, 0X5DFD,

0XB58B, 0XA402, 0X9699, 0X8710, 0XF3AF, 0XE226, 0XD0BD, 0XC134,

0X39C3, 0X284A, 0X1AD1, 0X0B58, 0X7FE7, 0X6E6E, 0X5CF5, 0X4D7C,

0XC60C, 0XD785, 0XE51E, 0XF497, 0X8028, 0X91A1, 0XA33A, 0XB2B3,

0X4A44, 0X5BCD, 0X6956, 0X78DF, 0X0C60, 0X1DE9, 0X2F72, 0X3EFB,

0XD68D, 0XC704, 0XF59F, 0XE416, 0X90A9, 0X8120, 0XB3BB, 0XA232,

0X5AC5, 0X4B4C, 0X79D7, 0X685E, 0X1CE1, 0X0D68, 0X3FF3, 0X2E7A,

0XE70E, 0XF687, 0XC41C, 0XD595, 0XA12A, 0XB0A3, 0X8238, 0X93B1,

0X6B46, 0X7ACF, 0X4854, 0X59DD, 0X2D62, 0X3CEB, 0X0E70, 0X1FF9,

0XF78F, 0XE606, 0XD49D, 0XC514, 0XB1AB, 0XA022, 0X92B9, 0X8330,

0X7BC7, 0X6A4E, 0X58D5, 0X495C, 0X3DE3, 0X2C6A, 0X1EF1, 0X0F78,

};

//  calculate the 16-bit CRC of data with predetermined length.

U16 GetCrc16(const U8* pData, int nLength)

{

U16  fcs  =  0xffff;         //  initialization

while(nLength>0){

fcs = (fcs >> 8) ^ crctab16[(fcs ^ *pData) & 0xff];

nLength--;

pData++;

}

return  ~fcs;         //  negated

}

# 9. Appendix B: a fragment of example of data packet of communication protocol

The following data displayed in hexadecimal are intercepted from the communication between a terminal and a server, wherein transmission means sending by the terminal and reception means returned from the server:

Transmission:  78 78 0F 01 03 53 41 90 31 64 49 53 10 0B 00 01 A3 67 0D 0A

Reception: 78 78 05 01 00 01 D9 DC 0D 0A

Transmission: 78 78 15 11 0B 03 1A 0B 0B 15 01 CC 00 26 6A 00 1D F1 00 01 00 02 A9 D0 0D 0A

Reception:78 78 05 11 00 02 6E D2 0D 0A

Transmission: 78 78 19 10 0B 03 1A 0C 04 27 C2 02 7A 93 C5 0C 46 69 59 00 15 37 00 01 00 2E 1E CF 0D 0A

Reception:78 78 05 10 00 2E DF 60 0D 0A

Transmission: 78 78 0A 13 00 06 04 00 01 00 03 D9 D2 0D 0A

Reception:78 78 05 13 00 03 CA E3 0D 0A

Transmission: 78 78 24 17 01 CC 00 26 6A 00 1D F1 31 32 35 32 30 31 35 39 31 36 33 35 37 31 38 36 00 00 00 00 00 00 01 00 0B 90 5D 0D 0A

Reception:78 78 72 17 6C 00 00 00 01 41 44 44 52 45 53 53 26 26 62 40 59 04 4F 4D 7F 6E 00 3A 5E 7F 4E 1C 77 01 60 E0 5D DE 5E 02 4E 91 5C 71 89 7F 8D EF 00 28 00 4E 00 32 00 33 00 2E 00 31 00 31 00 31 00 2C 00 45 00 31 00 31 00 34 00 2E 00 34 00 30 00 39 00 29 96 44 8F D1 26 26 31 32 35 32 30 31 35 39 31 36 33 35 37 31 38 36 00 00 00 00 00 23 23 00 0B BB F5 0D 0A

Transmission: 78 78 2E 1A 0B 03 1A 0E 2D 10 C2 02 7A CA 01 0C 46 59 1E 00 14 00 31 32 35 32 30 31 35 39 31 36 33 35 37 31 38 36 00 00 00 00 00 00 01 00 0C D1 91 0D 0A

Reception:78 78 76 17 70 00 00 00 01 41 44 44 52 45 53 53 26 26 7C BE 78 6E 5B 9A 4F 4D 00 3A 5E 7F 4E 1C 77 01 60 E0 5D DE 5E 02 4E 91 5C 71 89 7F 8D EF 00 28 00 4E 00 32 00 33 00 2E 00 31 00 31 00 31 00 39 00 36 00 2C 00 45 00 31 00 31 00 34 00 2E 00 34 00 30 00 39 00 34 00 30 00 29 26 26 31 32 35 32 30 31 35 39 31 36 33 35 37 31 38 36 00 00 00 00 00 23 23 00 0C 1A 87 0D 0A

Transmission: 78 78 12 19 01 CC 00 26 6A 00 1D F1 20 06 04 00 01 00 1B 88 01 0D 0A

Reception:78 78 71 17 6B 00 00 00 01 41 44 44 52 45 53 53 26 26 7D 27 60 25 54 7C 53 EB 00 3A 5E 7F 4E 1C 77 01 60 E0 5D DE 5E 02 4E 91 5C 71 89 7F 8D EF 00 28 00 4E 00 32 00 33 00 2E 00 31 00 31 00 31 00 2C 00 45 00 31 00 31 00 34 00 2E 00 34 00 30 00 39 00 29 96 44 8F D1 26 26 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 23 23 00 1B 28 F4 0D 0A

Transmission: 78 78 25 16 0B 03 1A 0F 0E 30 CF 02 7A C9 7D 0C 46 57 92 04 15 53 09 01 CC 00 26 6A 00 1D F1 29 06 04 00 01 00 13 6A DC 0D 0A

Reception: 78 78 75 17 6F 00 00 00 01 41 44 44 52 45 53 53 26 26 97 07 52 A8 62 A5 8B 66 00 3A 5E 7F 4E 1C 77 01 60 E0 5D DE 5E 02 4E 91 5C 71 89 7F 8D EF 00 28 00 4E 00 32 00 33 00 2E 00 31 00 31 00 31 00 38 00 39 00 2C 00 45 00 31 00 31 00 34 00 2E 00 34 00 30 00 39 00 31 00 38 00 29 26 26 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 23 23 00 13 70 A8 0D 0A

The specified meaning of above commands can be found in the protocol document.

# 10. Appendix C: Complete format of information package

A．Data packet sent by the terminal to the server

|  | Description | Bits | Example |
| --- | --- | --- | --- |
| Login Message Packet (20 Byte) | Start Bit | 2 | 0x78 0x78 |
|  | Packet Length | 1 | 0x0F |
|  | Protocol Number | 1 | 0x01 |
|  | Info content | Terminal ID | 8 | 0x01 0x23 0x45 0x67 0x89 0x01 0x23 0x45 |
|  |  | Type Identifier | 2 | 0x10 0x0B |
|  | Time zone language |  |  |
|  | Information Serial Number | 2 | 0x00 0x01 |
|  | Error Check | 2 | 0xA3 0x67 |
|  | Stop Bit | 2 | 0x0D 0x0A |

|  | Format | Length(Byte) | Example |
| --- | --- | --- | --- |
| GPS information packet (28+N Byte) | Start Bit | 2 | 0x78 0x78 |
|  | Packet Length | 1 | 0x1F |
|  | Protocol Number | 1 | 0x10 |
|  | Information Content | Date Time | 6 | 0x0B 0x08 0x1D 0x11 0x2E 0x10 |
|  |  | GPS message length, Quantity of GPS satellites | 1 | 0x9C |
|  |  | Latitude | 4 | 0x02 0x7A 0xC7 0xEB |
|  |  | Longitude | 4 | 0x0C 0x46 0x58 0x49 |
|  |  | Speed | 1 | 0x00 |
|  |  | Course, Status | 2 | 0x14 0x8F |
|  |  | Reserved extension bit | N | 0x00 0x01 |
|  | Serial Number | 2 | 0x00 0x03 |
|  | Error Check | 2 | 0x80 0x81 |
|  | Stop Bit | 2 | 0x0D 0x0A |

| LBS information packet （24+N Byte） | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
|  | Start Bit | 2 | 0x78 0x78 |
|  | Packet Length | 1 | 0x15 |
|  | Protocol Number | 1 | 0x11 |
|  | Date Time | 6 | 0x00 0x00 0x00 0x00 0x00 0x00 |
|  | Info content | MCC | 2 | 0x01 0xCC |
|  |  | MNC | 1 | 0x00 |
|  |  | LAC | 2 | 0x26 0x6A |
|  |  | Cell ID | 3 | 0x00 0x1D 0xF1 |
|  |  | Reserved extension bit | N | 0x00 0x01 |
|  | Serial Number | 2 | 0x00 0x18 |
|  | Error Check | 2 | 0x91 0x88 |
|  | Stop Bit | 2 | 0x0D 0x0A |

| Format | Length (Byte) | Example |
| --- | --- | --- |
| Status information packet (13+N Byte) | Start Bit | 2 | 0x78 0x78 |
|  | Packet Length | 1 | 0x0A |
|  | Protocol Number | 1 | 0x13 |
|  | Information Content | Terminal Information | 1 | 0x40 |
|  |  | Voltage Level | 1 | 0x06 |
|  |  | GSM Signal Strength | 1 | 0x04 |
|  |  | Reserved extension bit | N | 0x00 0x01 |
|  | Serial Number | 2 | 0x00 0x1F |
|  | Error Check | 2 | 0xC4 0x39 |
|  | Stop Bit | 2 | 0x0D 0x0A |

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| GPS, LBS, Status information packet（40+M+N+L Byte） | Start Bit | 2 | 0x78 0x78 |
|  | Packet Length | 1 | 0x0A |
|  | Protocol Number | 1 | 0x16 |
|  | Information Content | Date Time | 6 | 0x0B 0x08 0x1D 0x11 0x2E 0x10 |
|  |  | GPS Information | GPS information length, Quantity of GPS information satellites | 1 | 0x9C |
|  |  |  | Latitude | 4 | 0x02 0x7A 0xC7 0xEB |
|  |  |  | Longitude | 4 | 0x0C 0x46 0x58 0x49 |
|  |  |  | Speed | 1 | 0x00 |
|  |  |  | Course, Status | 2 | 0x14 0x8F |
|  |  |  | Reserved extension bit | M |  |
|  |  | LBS Information | LBS Length | 1 | 0x08 |
|  |  |  | MCC | 2 | 0x01 0xCC |
|  |  |  | MNC | 1 | 0x00 |
|  |  |  | LAC | 2 | 0x26 0x6A |
|  |  |  | Cell ID | 3 | 0x00 0x1D 0xF1 |
|  |  |  | Reserved extension bit | N |  |
|  |  | Status Information | Terminal Information Content | 1 | 0x40 |
|  |  |  | Voltage Level | 1 | 0x06 |
|  |  |  | GSM Signal Strength | 1 | 0x04 |
|  | Reserved extension bit | L | 0x00 0x1F |
|  | Serial Number | 2 | 0xC4 0x39 |
|  | Error Check | 2 | 0x0D 0x0A |
|  | Stop Bit | 2 | 0x00 0x1F |

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| LBS, phone number checking location info package | Start Bit | 2 | 0x78 0x78 |
|  | Packet Length | 1 | 0x1F |
|  | Protocol Number | 1 | 0x17 |
|  | Info content | LBS info | MCC | 2 | 0x01 0xCC |
|  |  |  | MNC | 1 | 0x00 |
|  |  |  | LAC | 2 | 0x26 0x6A |
|  |  |  | Cell ID | 3 | 0x00 0x1D 0xF1 |
|  |  | Phone number | 21 |  |
|  |  | Reserved extension bit | N |  |
|  | Serial Number | 2 | 0x00 0x03 |
|  | Check Bit | 2 | 0x80 0x81 |
|  | Stop Bit | 2 | 0x0D 0x0A |

B．Data Packet Sent by Server to Terminal

|  | Format | Length(Byte) | Example |
| --- | --- | --- | --- |
| Server response （10 Byte） | Start Bit | 2 | 0x78 0x78 |
|  | Data Bit Length | 1 | 0x01 |
|  | Protocol Number | 1 | 0x16 |
|  | Serial Number | 2 | 0x00 0x01 |
|  | Error Check | 2 | 0xD9 0xDC |
|  | Stop Bit | 2 | 0x0D 0x0A |

|  | Format | Length (Byte) | Example |
| --- | --- | --- | --- |
| Command packet sent from the server to the terminal （15+M Byte） | Start Bit | 2 | 0x78 0x78 |
|  | Packet length | 1 | 0x84 |
|  | Protocol Number | 1 | 0x16 |
|  | Information Content | Length of Command | 1 | 0x7E |
|  |  | Server Flag Bit | 4 | 0x00 0x00 0x00 0x01 |
|  |  | Command content | M |  |
|  |  | Reserved extension bit | 0 |  |
|  | Information Serial Number | 2 | 0x00 0x01 |
|  | Check Bit | 2 | 0xD9 0xDC |
|  | Stop Bit | 2 | 0x0D 0x0A |

ShenZhen Concox Information Technology CO.,Ltd

Tel: +86 755 2912 1200

Fax: +86 755 2912 1290

E-mail: aven@concox.cn.

Add: 4/F, Building B, Gaoxinqi Industrial Park,

Liuxian 1st Road, No.67 Bao'an District, Shenzhen

# Text boxes

Version：V1.82

Confidential